## Slide 1: Gyroscopic attitude control systems
Stepan Tkachev

## Slide 2: Introduction
Attitude control systems
Passive
Active
Gravitational
Magnetic
Magnetic
Gyroscopic
Thrusters

## Slide 3: Introduction
Attitude control systems
Need fields
Independent
Gravitational
Magnetic
Gyroscopic
Thrusters

## Slide 4: Introduction
Attitude control systems
Need fields
Independent
Gravitational
Magnetic
Gyroscopic
Thrusters

## Slide 5: What are gyroscopic systems?
Cell phone vibration motor
Spacecraft reaction wheel

## Slide 6: Principle of operation
Angular momentum conservation law
Control torque
You can create torque by
accelerating or decelerating
changing the angular momentum direction

## Slide 7: Reaction wheels
Axis of rotation is fixed
Main dynamical properties:
maximum torque
maximum angular momentum or spin rate

## Slide 8: Saturation and desaturation
Control can be created only when angular rate is varied
You lost controllability when you can’t change the angular rate
Too small spin rate
Too high spin rate
Saturation
Need additional algorithms for desaturation
Magnetic control system
Thrusters

## Slide 9: Gyroscopes
Axis of rotation can change its direction
Single gimbal control momentum gyro (SGCMG)
Dual gimbal control momentum gyro (DGCMG)
Main dynamical properties:
flywheel angular momentum
maximum gimbal spin rate

## Slide 10: Single gimbal CMG

## Slide 11: Single gimbal CMG
Pyramid type

## Slide 12: Attitude control system operation
State identification
Control torque calculation
Control application
Angular momentum calculation
Gimbal angles calculation
Steering law

## Slide 13: Steering law & singularities
Lost controllability
Singularity avoidance algorithm

## Slide 14: Illustrative example

## Slide 15: RW vs. SGCMG vs. DGCMG
 | Reaction wheels | SGCMG | DGCMG
Hardware complexity | simple | complex | very complex
Algorithms | simple | very complex | complex
Output torque | small | big | big
Miniaturization | possible | possible | impossible